## Slide 1: Material Properties.
Week 3

## Slide 2
Malleability

## Slide 3: Malleability
The ability of a material to be shaped and formed to a required shape or form.
Altered in any direction by compressive forces.
Hammering, pressing, rolling or bending.
Without rupturing or failing.
Malleable materials need not be strong but must be highly plastic.

## Slide 4
Toughness

## Slide 5: Toughness.
The ability of a material to withstand sudden impact loads without failing.
Eg: hammer blows, cold forming etc.
Materials that are tough will withstand bending & shearing without cracking.
Although not repeated in the same area.

## Slide 6
          Brittleness

## Slide 7: Brittleness.
This is the opposite of toughness.
Brittle material will crack and fail before it bends.
Tendency to fracture without much distortion.
It has little or none elastic properties.
The material is not ductile.

## Slide 8
Plasticity

## Slide 9: Plasticity.
The ability of a material to not permanently change shape whilst subjected to forces.
Some materials become plastic when they are overloaded and remain in the changed state.
Thus the new shape is maintained after loading.

## Slide 10
Elasticity

## Slide 11: Elasticity.
When materials are subjected to forces they will change shape.
To be elastic, the material must return to its original shape when the loading is removed.
Most materials are safe to use in their elastic state.
An example is a spring, which has to be elastic to work.

## Slide 12
Strength

## Slide 13: Strength.
Ability of a material to be subjected to loading.
Tensile, Compression & Shear.
Once these properties have been exceeded the material will either, fracture, buckle or shear.
A materials strength determines its use.
With correct design etc and these factors built in, the strength of a material and its use are many. Eg: Supporting heavy loads.

## Slide 14
Hardness

## Slide 15: Hardness.
The ability of a material to withstand.
Abrasive wear, surface indentation or scratching.
A drill or lathe tool has to be harder than the material it is cutting.

## Slide 16
Ductility

## Slide 17: Ductility.
The ability of a material to be drawn and stretched into long thin shapes reducing its cross sectional area.
Copper has the ability to be drawn into wire.
Ductile materials must be highly plastic.
The material must not fail when being stretched or drawn into shape.

## Slide 18
Conductivity

## Slide 19: Conductivity.
A materials ability to conduct heat or an electric current.
Copper widely used in the form of wires.
Aluminium conducts heat rapidly when welded.
Certain coatings can be applied to reduce heat conductivity on exposed surfaces.