## Slide 1: Polymeric Materials.

## Slide 2: Groups of Polymeric Materials.
Thermosetting Plastics (Thermosets).
Thermoplastics.
Elastomers.

## Slide 3: Thermosets.
This group of polymeric materials undergoes chemical change during the moulding process and can never again be softened by heating.
They are generally hard and rigid and rather brittle.
Typical example is melamine formaldehyde.
Snooker balls, electrical fittings etc.

## Slide 4: Thermoplastics.
These become soft and can be remoulded each time they are reheated.
They are not so rigid as thermosetting plastics but tend to be soft.
Eg. Rigid polymerised vinyl chloride (pvc) used for guttering and downpipes on building.
Can also be soft and pliable, such as non-rigid pvc used in insulation of flexible cables.

## Slide 5: Elastomers.
Elastomers or rubbers are cross linked polymeric materials in which there are not sufficiently cross linked to make them rigid like thermosets.
Where as thermosets show little elongation under stress, elastomers are capable of extreme elastic deformation.
Elastomers are usually addition polymerised as thermoplastics then cross linked with sulphur.

## Slide 6: Elastomers.
Increased vulcanisation increases the cross linking and this in turn increases the stiffness and reduces the elongation properties of the material.
Fully vulcanised natural rubber becomes a rigid brittle thermoset called ebonite.