## Slide 1: Wk 8/9
Material Specification, Standard Data & Forms of Supply.

## Slide 2: Material Specification
As already discussed as engineers we have to consider many aspects of the behaviour of the material when selected for a given application or component.
Will it be satisfactory for use?
Is the overall cost a factor?
Etc, etc.

## Slide 3: Material Specification
We have to investigate whether the material has all the required characteristics and properties relevant to its intended use.

## Slide 4: Criteria for selecting materials
Commercial factors such as:
Cost
Availability
Ease of manufacture

## Slide 5: Criteria for selecting materials
Engineering properties of materials such as:
Electrical conductivity
Strength
Toughness
Ease of forming by extrusion, forging & casting
Machinability
Corrosion resistance etc

## Slide 6: Material Mechanical Properties
The mechanical properties of a material describe how it will react to physical forces. Mechanical properties occur as a result of the physical properties inherent to each material, and are determined through a series of standardized mechanical tests.

## Slide 7: Mechanical Properties
Tensile Strength This is the ability of a material to withstand tensile loads without rupture when the material is in tension
Compressive Strength This is the ability of a material to withstand Compressive (squeezing) loads without being crushed when the material is in compression .
Shear Strength This is the ability of a material to withstand offset or traverse loads without rupture occurring .
Toughness This is the ability of a material to withstand shatter. A material which easily shatters is brittle. Toughness indicates the ability of a material to absorb energy
Elasticity This is the ability of a material to deform under load and return to its original size and shape when the load is removed. The property is required for springs

## Slide 8: Mechancial Properties
Plasticity This is the property of a material to deform permanently under the application of a load. Plastacine is plastic. This is the exact opposite to elasticity.
Ductility This is ability of a material to stretch under the application of tensile load and retain the deformed shape on the removal of the load. A ductile material combines the properties of plasticity and tensile strength. All materials which are formed by drawing are required to be ductile
Malleability This is the property of a material to deform permanently under the application of a compressive load. A material which is forged to its final shape is required to be malleable
Fatigue Strength This is the property of a material to withstand continuously varying and alternating loads

## Slide 9: Physical Properties
In addition to the mechanical properties just discussed, the design of an engineered product may require other properties such as electrical or thermal conductivity to be taken into account.

## Slide 10: Physical Properties
Other properties of importance are: Density, Melting Temperature, Chemical Stability, Magnetic Properties etc.
These are referred to as the ‘physical properties’ and will now be considered.

## Slide 11: Physical Properties.
Density – is defines as mass per unit volume for a material. The derived unit usually used by engineers is kg/m³
Lists and data sheets are available for cross referencing various materials and their corresponding density.

## Slide 12: Melting Temperatures
The melting point of a solid is the temperature at which it changes state from solid to liquid. At the melting point the solid and liquid phase exist in equilibrium.

## Slide 13: Quick Check
List and describe 4 mechanical properties of a material.
Sketch and describe the difference between a tensile strength, compressive strength and shear strength.
Describe the melting point of a material and give an example and application of why and how its used in manufacturing.

## Slide 14: Electrical Properties
Conductivity- An example of a copper wire
Copper has been chosen for the conductor of the core of the cable because copper has the property of very good electrical conductivity.
That is it offers little resistance to the flow of electrons.
Namely the electric current.

## Slide 15: Electrical Properties
A plastic material such as polymerised vinyl chloride (PVC) has been chosen as the insulating sheathing around the outside of the wire conductor.
The material has been chosen because it is such a bad conductor and very few electrons can pass through it. (Insulator)
There is no such thing as a perfect insulator, only a very bad conductor.

## Slide 16: Electrical Properties
Other electrical properties worth investigating and getting a basic definition would be:
Semiconductors.
Permittivity.

## Slide 17: Magnetic Properties
Reluctance – As previously discussed some materials are good and bad conductors of electricity in exactly the same way that some materials can be good or bad conductors of magnetism.
The resistance of a magnetic circuit is referred to as reluctance.
Good magnetic conductors have a low reluctance such as ferrous metals.

## Slide 18: Magnetic Properties
Other magnetic properties worth investigating and getting a basic definition would be:
Permeability
Hysteresis
Hard Magnetic
Soft Magnetic

## Slide 19: Thermal Properties
Conductivity
Expansivity
Fusability
Temperature Stability.

## Slide 20: Material Specification
A specification (often abbreviated as spec) is an explicit set of requirements to be satisfied by a material, product, or service.
Should a material, product or service fail to meet one or more of the applicable specifications, it may be referred to as being out of specification.

## Slide 21: Material Specification
Specifications are a type of technical standard.
A technical specification may be developed by any of various kinds of organizations, both public and private.
Suppliers, Organisations, Governments, Military etc.

## Slide 22: Material Data Sheets
A data sheet describes the technical characteristics of an item or product. It can be published by a manufacturer to help people choose products or to help use the products.
This data can also be incorporated into safety sheets which highlight the properties of a certain substance or material.

## Slide 23: Material Data Sheets
These are an important component of product stewardship and workplace safety, it is intended to provide workers and emergency personnel with procedures for handling or working with that substance in a safe manner, and includes information such as physical data (melting point, boiling point, flash point, etc.), toxicity, health effects, first aid, reactivity, storage, disposal, protective equipment, and spill-handling procedures. MSDS formats can vary from source to source within a country depending on national requirement.

## Slide 24: Availability/Manufacturability
Availability and manufacturability requirements are often unseen limiting factors in materials selection. The importance of a material being available is obvious. Materials which are not available cannot be used. The importance of processibility is not always so obvious.

## Slide 25: Availability/Manufacturability
Any other desirable qualities are useless if a material cannot be processed into the shape required to perform its function. Most engineering materials in use today have well known substitutes which would perform better and often at lower cost but processes for forming, cutting, machining, joining, etc. are not available or commercially viable

## Slide 26: Availability/Manufacturability
There is often a period of time after a new material is introduced during which its application is severely limited while processing techniques are developed which facilitate its use.

## Slide 27: Material Cost
A materials cost is also generally a limiting factor. While cost is universally recognized and perhaps the easiest of all properties to understand there are specific cost considerations for materials selection. Just as materials and their processing go hand in hand so do material costs and processing costs. Understanding the entire processing sequence is critical to accurately evaluating the true cost of a material.

## Slide 28: Summary
As we begin the 21st century, advances in materials research and technology offer great promise. Materials Science forms the foundation for engineers in product development because the structures, components, and devices that engineers design are limited by the properties of the materials that are available and the techniques that can be used for fabrication.